## Slide 1: Arduino Soil Moisture Probe
Tyler Brown and Evan Lesmez

## Slide 2: Goals
Remotely monitor soil moisture in Engineer’s Way bioretention system
  Relate soil moisture data to rainfall events and optimize water flow
Create a soil moisture probe using cheap and readily available equipment
Make a product that is easily reproduced and can be used in a variety of applications
  Homes, gardens, irrigation systems, etc.

## Slide 3: Equipment
Total Cost: $20
NRF24L01 Radio Transmitter (2x)
WINGONEER YL-69 Sensor and HC-38 Module
Arduino Uno Board (2x)
AA Battery Pack (connects 6 in series)
Colored Wire with pins for Arduino (18x)

## Slide 4: Setup
Moisture Probe, Arduino, Radio Transmitter, and battery pack deployed in bioretention system
  Waterproof plastic container with slot for probe
Radio receiver and Arduino connected to PC in Thornton B-Wing
Probe gathers moisture data, transmits to receiver, and uploads to PC
  All data sent to Blynk server, which can be viewed via Blynk mobile app

## Slide 6: Program
All coding in the Arduino IDE, required importing different libraries all shown in the Git repository:
  RF24 for radio communication
  Blynk for posting data to server
Only two scripts required
  Transmitter records and sends data (RadioTransmit)
  Receiver records and uploads data (RadioBlynkReceive)
https://github.com/uva-hydroinformatics/Soil_moisture_and_Rainfall_sensing

## Slide 7: Testing
Put the transmitter setup out in the rain garden for a week
  Receiver was in nearby room hooked up to a computer
  Data was recorded and posted every 30 seconds
  Blynk app: utilized history graph widget
Soil moisture levels were obtained and plotted in real time

## Slide 8: Results
Overall successful. Soil moisture plotted over the course of a week
  Data collected & posted on the Blynk-server
  Exported to a CSV and graphed →
  Demonstrated at the UVA SEAS open house
Rapid data collection
Instant plotting

## Slide 9: Obstacles and Solutions
Probe Calibration
  Code must scale probe output to match actual moisture levels. Calibrated with pure water (100%) and a dry paper towel (0%)
Radio Transmission Range
  Short range boosted with soldered antennas
  Arduino Shield offers wifi capability for future projects
Battery Life
  Frequent transmission drains batteries quickly (roughly 30,000 transmissions per battery pack)
  Storing data locally and sending less frequent packets dramatically increases lifetime

## Slide 10: Future Work
Pair with tipping bucket that measures rainfall intensity and depth
  Correlate rainfall depth with soil moisture levels, increase predictability
  Similar wireless transmission and data logging
Use probe to automate valve controls
  Moisture too high → Open drainage valves
  Low moisture → close valves, activate sprinklers, etc.
Improve sturdiness of design
  Solder pins, build robust container, larger battery pack